## Slide 1: Smartphone Controlled Robot Assembly

## Slide 2: Smartphone Controlled Robot
In a smartphone-controlled robot, the motion of the robot is controlled using the inputs of a smartphone app – Dabble. We will use the gamepad module to control the robot.

## Slide 3
Assembly of the Robot

## Slide 4: Components
Wheel
Motor Bracket
DC Motor
Base Plate
Bolt
Nut
Screw Driver

## Slide 5: Base Plate
You will mount the motor clamps and the caster wheel directly to the base plate. You have to mount motor on the opposite side of the evive logo.

## Slide 6: STEP 1
Fix the motor mounting brackets to the chassis using M3 bolts of 8mm length and M3 nuts.

## Slide 7: STEP 1
Fix the motor mounting brackets to the chassis using M3 bolts of 8mm length and M3 nuts.

## Slide 8: STEP 2
Attach the two motors, one to each bracket, side by side and fasten using M3 bolts of 25mm length and M3 nuts.

## Slide 9: STEP 2
Attach the two motors, one to each bracket, side by side and fasten using M3 bolts of 20mm length and M3 nuts.

## Slide 10: STEP 3
Now, fit the wheels into the motor shafts.

## Slide 11: STEP 3
Now, fit the wheels into the motor shafts.

## Slide 12: STEP 4
Mount the M3 standoffs (20 mm) on the chassis using M3 bolts of 8mm length.

## Slide 13: STEP 4
Mount the M3 standoffs (20 mm) on the chassis using M3 bolts of 8mm length.

## Slide 14: STEP 5
Bring the Castor on top of the standoffs in the configuration shown and fasten using M3 bolts of 12 mm length.

## Slide 15: STEP 5
Bring the Castor on top of the standoffs in the configuration shown and fasten using M3 bolts of 12 mm length.

## Slide 16: STEP 6
Using the holes on the back of evive, fasten it to the chassis using M3 bolts of 12mm length.

## Slide 17: STEP 6
Using the holes on the back of evive, fasten it to the chassis using M3 bolts of 12mm length.

## Slide 18: STEP 6
Using the holes on the back of evive, fasten it to the chassis using M3 bolts of 12mm length.

## Slide 19: Your Robot is Ready !