## Slide 1: DIY Goggles

## Slide 2: DIY Goggles
In this activity, you will make a goggle which can open or close the shades using servo motor.

## Slide 3: Steps
Cut the following pieces from the Cardboard:
2 pieces of 15 cm x 6 cm - Part A
1 piece of 9 cm x 2 cm - Part B
1 piece of 4 cm x 2 cm - Part C
1 piece of 6 cm x 2 cm - Part D
1 piece of 6 cm x 3 cm - Part E

## Slide 4: Steps
Also, cut a small piece of straw of 2cm length.

## Slide 5: Steps
Now, take one Part A and cut it in the shape of goggles.

## Slide 6: Steps
Then, take part D and paste it on one side. Next, take a small piece of straw and paste it on the other side.

## Slide 7: Steps
Next, cut holes in the second Part A.

## Slide 8: Steps
Next, cut holes in the second Part A.

## Slide 9: Steps
Then take the smallest cut out, i.e. Part C and paste it on one of the sides of Part A with holes cut in it.

## Slide 10: Steps
Take two straws and paste them on both the sides of the back frame, i.e. Part A that has holes cut in it.

## Slide 11: Steps
Then, take Part B and wrap it around the servo and paste the two ends with glue.

## Slide 12: Steps
Then, take the single sided servo horn and fix it on the servo head using the self-threading screw; the horn and the screw are available with the servo accessories.

## Slide 13: Steps
Next, take Part E piece and make a small hole in it. Then, paste the servo and Part E piece on the larger piece with holes cut out as shown:

## Slide 14: Steps
Finally, join the two large cutouts by fixing the small straw in the hole and insert the servo horn the Part D of the sunglasses and fix the assemblies using hot glue.

## Slide 15: Steps
Connect the three servo wires to servo motor channel S1. Make sure that the brown wire is connected to the leftmost pin.

## Slide 16: Steps
Now, switch evive ON, navigate through the controls menu and select Servo 1. Now, turn the potentiometer knob and watch the goggles do their magic!